15 mm

4.	[D13B2 EUROPE & KQ Engine]

Using a 5/32" or 4.1 mm diameter drill, drill out the rivets and remove the choke cover.

CAUTION: Cover the carburetor with a clean shop rag to prevent chips from falling into the carburetor throat.

[D12B1, D13B3 EXCEPT EUROPE and D15B3 Engine]

Remove the screws and remove the choke cover.

5.	Reinstall the cover and adjust it so that index marks
align (D13B2 EUROPE & KQ Engine:, then secure it
with rivets).

CHOKE COVER

CHOKE COVER

7.   Reconnect the connector and reinstall the air cleaner.

11-125

6.   Connect the respective terminals to a new connector and install a new terminal retainer.

NOTE:

•	Be sure to connect the terminal before installing the terminal retainer.

•	Replace the connector and terminal retainer with the new ones.

•	Note the location of the terminal.